## Slide 1: DEPI Final Project
Fortinet Cybersecurity Engineer

## Slide 2: Agenda
1 – what is VPN
2- site to site VPN
3 – ipsec VPN
4 – implementation and simple topology

## Slide 3: What is VPN ?
A VPN (Virtual Private Network):
is a technology that creates a secure and encrypted connection over a less secure network, such as the internet. VPNs are used to enhance privacy, protect sensitive data, and enable secure communication. They work by encrypting your data and routing it through a remote server, hiding your IP address and online activities.

## Slide 4: Type of VPN:
1. Remote Access VPN
  Purpose: Enables users to securely connect to a private network (e.g., an office network) from a remote location.
2. Site-to-Site VPN
  Purpose: Connects entire networks (e.g., two office branches) over the internet securely.
3. Client-to-Site VPN
  Purpose: Similar to remote access but more tailored to individual users needing direct access to a corporate network.

## Slide 5: Type of VPN:
4. SSL VPN (Secure Sockets Layer VPN)
  Purpose: Provides secure remote access without requiring specialized software.
5. MPLS VPN (Multiprotocol Label Switching VPN)
  Purpose: Uses MPLS technology to connect different locations over a service provider's private network.
6. Mobile VPN
  Purpose: Designed for users on mobile devices who frequently switch between networks or maintain active sessions.

## Slide 6: Type of VPN:
7. Cloud VPN
  Purpose: Extends secure connections to cloud environments.
8. Peer-to-Peer (P2P) VPN
  Purpose: Used for secure file sharing or decentralized network setups.

## Slide 7: VPN Protocols
VPNs can also be categorized based on the protocols they use:
OpenVPN: Open-source, highly secure, and flexible.
IKEv2/IPsec: Secure and stable, especially for mobile devices.
L2TP/IPsec: A combination of Layer 2 Tunneling Protocol and IPsec encryption.
PPTP: Fast but outdated and less secure.
WireGuard: Modern, lightweight, and efficient.

## Slide 8: Site To Site VPN:
Purpose: Connects entire networks (e.g., two office branches) over the internet securely.
Use Case: Large organizations that need to interconnect geographically separated networks.
  How It Works:
Establishes a secure tunnel between routers or gateways of two networks.
Subtypes:
  Intranet-based Site-to-Site VPN: Connects different branches of the same organization.
  Extranet-based Site-to-Site VPN: Connects an organization’s network with that of a partner organization.

## Slide 9: IPsec VPN Site TO Site:
What is IPsec? When should you use it?
  IPsec is a vendor-neutral set of standard protocols that is used to join two physically distinct LANs. The LANs are joined as if they were a single logical network, despite being separated by the internet.

## Slide 10: Site To Site Topologys:

## Slide 11
Simple Topology and implementation on EVE Environment

## Slide 12: Toplogy Will Work on

## Slide 13: Methods to make ipsec Tunnle
1 – Manually
2 – using Wizerd
So For simplicity we will use ipsec wizerd

## Slide 14: Ipsec using ipsec wizard in Fortigate:
Local Fortigate:
  Login:

## Slide 15: Go to vpn tab:
1 – select ipsec wizard
  Then fill the information about the Remote site

## Slide 16: Make the Authentication configuration

## Slide 17: Make routing policy for forward the traffic

## Slide 18: Finally review your configuration:

## Slide 19: The First VPN site ready:

## Slide 20: Go to the remote side the make the same conf

## Slide 21: Choose your Remote IP and the interface

## Slide 22: Choose what is the local and remote subnets:

## Slide 23: The Second site now ready:

## Slide 24: Back to the first site and show:
Because We use the wizard we just choose the configuration and don’t make any custome configuration
So let set the configuration that done automatically with using the wizard

## Slide 25: From the first side:
Static routes addes automatic:

## Slide 26: The policy created automatic:

## Slide 27: The secode or the remote site:
Static routes :

## Slide 28: The policy created automatic:

## Slide 29: Now Lets Test Connectivity

## Slide 30: Test Gatways:

## Slide 31: Test connectivity between hosts

## Slide 32: Finally make successful ipsec tunnels between two sites to secure the communication between them

## Slide 33: Q&A LinkedIn:www.linkedin.com/in/momen-ameer-7b3032233 mail: momenameer2003@gmail.com

## Slide 34: Thank you